## Slide 1: Adaptive Beam Measurement
Master thesis research 2020
Boqiang Wang & Harshal Patal A
CSIM-FsUe Team A
2020-10-30

## Slide 2
3GPP Baseline
Objective
Method
Simulation
Result
Content

## Slide 3: 3GPP Baseline

## Slide 4: 3GPP Baseline
TDD 4-1 Pattern

## Slide 5: 3GPP Baseline

## Slide 6: Objective
Beam management consumes a lot of resources
Try another approach compare to 3GPP baseline by using machine learning

## Slide 7: Method overview
Data collection using baseline algorithm in simulator
Train and evaluate ML algorithms offline
Integrate the prediction function for the 2 best algorithms into the simulator
Run simulations and collect KPIs

## Slide 8: Method

## Slide 9: Method

## Slide 10: Method
Machine Learning Algorithms Training:
12 SSB RSRP values
Angle of Arrival (2.5-degree accuracy from Product Implementation)
Timing Advance (9.8 meters accuracy from 3GPP)
4. Narrow beam index

## Slide 11: Methods explored in offline analysis
Support Vector Machines (SVM)
Accuracy : 80%
Logistic Regression (LR)
Accuracy : 65%
K-Nearest Neighbor (KNN)
Accuracy : 71%
Neural Network (NN)
Accuracy : 80%

## Slide 12: Limitation
Line of Sight (LoS)

## Slide 13: Simulation
Evaluate the accuracy of the machine learning algorithm
Compare Baseline and Prediction
Set Up simulator with the same seeds (By hard coding the seed in the simulator)
One single UE
Random Mover to move user into random positions

## Slide 14: Key performance indicators (KPIs)
 | Single UE (stationary at random positions) | Multi UE (Circular mover, different speeds and SSB intervals)
Accuracy : Narrow beam selection + RSRP |  | 
Throughput |  | 

## Slide 15: Results: Predicted Narrow Beam (1)
Cluster outliers are probably side lobes
Baseline vs Neural Network (Single UE)
Baseline vs SVM (Single UE)
 | NN | SVM
Correct Beam Prediction | 80% | 80.4%
Neighbor Beam Prediction | 18% | 19.2%
Bad Beam Prediction | 2% | 0.4%

## Slide 16: Results: Predicted Narrow Beam (2)
Baseline
Neural Network
Baseline vs Neural Network (Single UE)

## Slide 17: Results: Predicted Narrow Beam (2)
Baseline vs SVM (Single UE)
Baseline
SVM

## Slide 18: Results: RSRP distribution
Baseline vs Neural Network (Single UE)
Baseline vs SVM (Single UE)

## Slide 19: Future scope
Consider non line of sight scenario.
Test for beam reflections.
Figure out way to handle side lobes using ML.

## Slide 21: Backup Slide